## Slide 1: SWC II: Software Guide
PRESENTED BY Pokai, Hsieh, Research Project Team
Advanced Automation Solutions and Technologies 04.30.2018

## Slide 2: Flowchart of SWC II Software
- System structure.

## Slide 3: Flowchart of SWC II Software - System structure
SDK on Server/PC
SWC II
Function | Description
Connection(string strIP, string strPort) | strIP: destination IP; strPort: sourece port. Features: Connect to SWC II.
MsgSend(string str) | str: Command of SWC II. Features: Send command to SWC II.
MsgReceive() | Features: Receive command from SWC II.
DisConnection() | Features: Disconnect with SWC II.
:
From
Server/PC

## Slide 4: Flowchart of SWC II Software - System structure
Setting mode command:
Routine Mode command:
EQSId
EQBaudrate
EQType
EQCmd
From Server/PC
To
Routine Mode
EQId
EQData
From Server/PC
Once, if necessary.
Loop, till re-setting or Shutdown.

## Slide 5: Flowchart of SWC II Software
- Command explanation.

## Slide 6: Flowchart of SWC II Software - Command explanation
EQSId / EQId: To identify each equipment.
  Sending format of Server/PC:
  Example:
    EQSId*@192.168.0.90#1,0#2,0#3 0#4,0#5,0#6,0#7,0#8,0#9,0#10,0#11,0#12,0#&
    EQId*@192.168.0.90#1,0#2,0#3 0#4,0#5,0#6,0#7,0#8,0#9,0#10,0#11,0#12,0#&
Command | - | SWC IP | - | N-th Port | End char
EQSId/EQId | *@ | 192.168.0.100 | # | N,0 | #&

## Slide 7: Flowchart of SWC II Software - Command explanation
EQSId / EQId: To identify each equipment.(cont.)
  Receiving format of Server/PC:
  Example:
    EQSId*192.168.0.90#1,SN00021#2,SN00005#3,FF#4,SN00003#5,SN00100#6,FF#7,FF#8,SN00110#9,SN00201#10,SN00111#11,SN00006#12,SN00007*&
    EQId*192.168.0.90#1,SN00021#2,SN00005#3,FF#4,SN00003#5,SN00100#6,FF#7,FF#8,SN00110#9,SN00201#10,SN00111#11,SN00006#12,SN00007*&
Command | - | SWC IP | - | N-th Port | End char
EQSId/EQId | * | 192.168.0.100 | # | OK: N,SN0001ABCD NG: N,FF | *&

## Slide 8: Flowchart of SWC II Software - Command explanation
EQBaudrate: Set baudrate of each equipment.
  Sending format of Server/PC:
  Example:
    EQBaudrate*#1,9600,8,N,1#2,115200,8,N,1#3,115200,8,N,1#4,115200,8,N,1#5,115200,8,N,1#6,115200,8,N,1#7,115200,8,N,1#8,115200,8,N,1#9,NULL,8,N,1#10,9600,8,N,1#11,9600,8,N,1#12,9600,8,N,1#&
Command | - | SWC IP | - | N-th Baudrate | End char
EQBaudrate | * | X | # | N,BaudRate,DataBits,Parity,StopBits | #&

## Slide 9: Flowchart of SWC II Software - Command explanation
EQBaudrate: Set baudrate of each equipment.(cont.)
  Receiving format of Server/PC:
  Example:
    EQBaudrate*192.168.0.90#1, 1#2, 1#3, 1#4, 0#5, 0#6, 1#7, 1#8, 0#9, 1#10, 1#11, 1#12, 0*&
Command | - | SWC IP | - | N-th Port | End char
EQBaudrate | * | 192.168.0.100 | # | OK: N, 1 NG: N, 0 | *&

## Slide 10: Flowchart of SWC II Software - Command explanation
EQType: To classify current equipment.
  Sending format of Server/PC:
  Example:
    EQType*@KCM$N6:1,2,5,6,7,8@Husky$N2:9,11@SDC15$N4:3,7,10,12@&
Command | - | SWC IP | - | Total Number x of Type | End char
EQType | * | X | @ | Type$Nx:x1,x2,…,xn | @&

## Slide 11: Flowchart of SWC II Software - Command explanation
EQType: To classify current equipment.(cont.)
  Receiving format of Server/PC:
  Example:
    EQType*192.168.0.90#OK*&
Command | - | SWC IP | - | Value | End char
EQType | * | 192.168.0.100 | # | OK | *&

## Slide 12: Flowchart of SWC II Software - Command explanation
EQCmd: Setting command of equipment.
  Sending format of Server/PC:
  Example:
    EQCmd*@KCM:010310010001D10A@Husky:04262031222005@Husky:04262032222005@Husky:04262033222005@Husky:04262034222005@Husky:04262035222005@Husky:04262036222005@Husky:04262037222005@Husky:04262038222005@Husky:04262039222005@Husky:0426203A222005@Husky:0426203B222005@Husky:0426203C222005@SDC15:0103238D00025FA4@SDC15:0203238D00025F97@SDC15:0303238D00025E46@SDC15:0403238D00025FF1@SDC15:0503238D00025E20@SDC15:0603238D00025E13@SDC15:0703238D00025FC2@SDC15:0803238D00025F3D@SDC15:0903238D00025EEC@SDC15:0A03238D00025EDF@SDC15:0B03238D00025F0E@SDC15:0C03238D00025EB9@&
Command | - | SWC IP | - | Command of Type | End char
EQCmd | * | X | @ | Type:SettingCommand | @&

## Slide 13: Flowchart of SWC II Software - Command explanation
EQCmd: Setting command of equipment.(cont.)
  Receiving format of Server/PC:
  Example:
    EQType*192.168.0.90#OK*&
Command | - | SWC IP | - | Value | End char
EQCmd | * | 192.168.0.100 | # | OK | *&

## Slide 14: Flowchart of SWC II Software - Command explanation
EQData: Get sensing data from each equipment.
  Sending format of Server/PC:
  Example:
    EQData*#12#&
Command | - | SWC IP | - | Total equipment numbers | End char
EQData | * | X | # | N | #&

## Slide 15: Flowchart of SWC II Software - Command explanation
EQData: Get sensing data from each equipment.(cont.)
  Receiving format of Server/PC:
  Example:
    EQData*192.168.0.90#1@01-03-02-00-10-5F- A4*... #7@01-03-02-00-10-5F-A4@02-03-02-00-10-5F-A4.. *…#11@01-03-02-00-10-5F-A4@02-03-02-00-10-5F-A4.. *&
Command | - | SWC IP | - | N-th Port | End char
EQData | * | 192.168.0.100 | # | OK: N, @data* NG: N, FF | *&

## Slide 16
Thank you for your attention!
PoKai, Hsieh • POKAI_HSIEH@JABIL.COM • WWW.JABIL.COM